## Slide 1: Python on GPUs
Geert Jan Bex
(geertjan.bex@uhasselt.be)
License: this presentation is released under the Creative Commons CC BY 4.0, see https://creativecommons.org/licenses/by/4.0/deed.ast

## Slide 2
https://gjbex.github.io/Python-on-GPUs/

## Slide 4: Typographical conventions I
Inline code fragments and file names are rendered as, e.g., hello_world.py
Longer code fragments are rendered as
Data files are rendered as
#!/usr/bin/env python
…
if __name__ == '__main__':
print('hello world!')
case dim temp
1 1 -0.5
2 1 0.0
3 1 0.5
4 2 -0.5
…
fragment not shown

## Slide 5: Typographical conventions II
Shell commands are rendered as
  Do not type $, it represents your shell prompt!
Good practice:
Bad practice:
(Potential) hazards/bugs:
Performance issue:
Performance boost:
Warning:
$ python –m doctest data_parsing.py

## Slide 6: What do GPUs look like?

## Slide 7: Host-device model
Compute node has
  1 or more CPUs
  Volatile memory: RAM
  PCIe bus with
    1 or more GPUs
Application
  Runs on host
  Offloads computations to device(s)
Host
Device(s)

## Slide 8: Offload model
Host
Device0
Device1


## Slide 9: Host-device model implications
Explicit data transfer between host and device
Explicit synchronization
  Avoid race conditions
Interconnect latency/bandwidth
  Potential performance bottleneck
Hardware details matter a lot!

## Slide 10: GPU hardware

## Slide 11: GPU Streaming Multiprocessor (SM)
4 Warp schedulers
Simple architecture
  No out-of-order execution
  No branch prediction
  No sophisticated control flow
Pipelines for
  FP32
  FP64
  INT
  Tensor
  LD/ST
Memory lanes for pipelines
4-byte registers (thread-private)
Block shared memory/L1 cache
Const/texture cache
Warp
=
32 threads, all execute same instruction

## Slide 12: GPU hardware execution model
SIMT: Single Instruction, Multiple Threads
32 threads grouped in warps (NVIDIA)/wavefronts (AMD)
Threads in warp execute same instruction on different data
Warp-group instructions (H100+)
  4 warps participate in tensor instruction
  Accommodate larger tensor cores & matrix tiles

## Slide 13: Branching on GPUs
Cheap if threads agree
Divergence leads to
  Masking of inactive threads
  Execution of both paths
Try to avoid branching
  Code structure
  Data layout
 performance loss
13

## Slide 14: Tensor cores
Computed as many small tiles
  C
Tile size depends on
  Type
  Compute capability
Performance: tensor core TFLOP/s >> CUDA core TFLOP/s
where , B
Input | 
FP16 | 1688
BF16 | 1688
TF32 | 1688
INT8 | 16832
FP64 | 884
Input | 
FP16 | 1688
BF16 | 1688
TF32 | 1688
INT8 | 16832
FP64 | 884
E.g., for A100

## Slide 15: Multiple SMs
GPU has many Streaming Multiprocessors
  E.g., A100: 108
Share
  L2 cache
  Global (GPU) memory
32 threads/warp  4 warp instructions/SM  number SMs for, e.g., A100 = 13,824 instructions/cycle
Massive parallelism!

## Slide 16: GPU memory hierarchy
Level | Scope | Managed by | Typical latency | Size (NVIDIA A100)
Registers | Thread | Compiler |  1 cycle | 256K  4b per SM
Shared memory | Block | Programmer |  10-20 cycles | Up to 164 Kb, part of 192 Kb
L1 cache | SM | Hardware | 30-40 cycles | 
Const/texture cache | SM | Hardware |  constant | 8 Kb
L2 cache | GPU | Hardware |  200 cycles | 40 Mb
Global (HBM) | GPU | Programmer |  400-800 cycles | 40 or 80 Gb
Regusters + shared memory  threads per block
Latency hiding through oversubscription

## Slide 17: Multiple GPUs/node, multiple nodes
Typically, 4 GPUs/node (A100)
  NVLink
    Direct connection between all GPUs
    12 NVLink lanes/GPU  4 lanes to each GPU
    50 Gb/lane (bi-directional)  200 Gb between GPUs
  PCIe connection to host
Infiniband connects nodes

## Slide 18: Bandwidth hierarchy
Global GPU memory  2 Tb/s
NVLink  200 Gb/s
PCIe  32 Gb/s
Host memory  300 Gb/s
Infiniband (HDR)  25 Gb/s
CPU
GPU0
HBM
GPU1
HBM
GPU2
HBM
GPU3
HBM
RAM
PCIe
NVLink
CPU
GPU0
HBM
GPU1
HBM
GPU2
HBM
GPU3
HBM
RAM
PCIe
NVLink
HDR

## Slide 19: Programming model

## Slide 20: Programming GPUs
CUDA on NVIDIA/HIP on AMD
C/C++/Fortran + OpenMP 5.x
C/C++/Fortran + OpenACC
SYCL
C++ + Kokkos


## Slide 21: Memory management
Explicit memory management
  Memory allocation/deallocation
  Host versus device addresses
  Explicit copy
    Host  device
    Device  host
    Device  device
  Explicit synchronization
Unified memory management
  Memory allocation/deallocation
  Single address space
  Implicit data migration (page fault/page copy)
  Explicit synchronization
More control, potentially better performance

## Slide 22: Kernels
Functions compiled for device
Operate on data in device memory
Launched from host, run on device
Configuration in 1D, 2D, 3D
  Threads per block
  Blocks per grid

## Slide 23: Threads, blocks & grid
Threads per block: x-dimension  y-dimension  z-dimension  1024
  x-dimension  1,024
  y-dimension  1,024
  z-dimension  64
Blocks per grid
  x-dimension  231 - 1
  y-dimension  65,535
  z-dimension  65,535
Warp is 32 threads, warp-group is 4  32 threads
Kernel can get
Thread indices, thread dimensions
Block indices, block dimension
 differentiate work/thread

## Slide 24: Streaming Multiprocessors & blocks
All threads in block execute on same SM
  Can be synchronized
  Can use shared memory
Multiple blocks assigned to SM
  Depends on registers, shared memory/L1 cache availability
Threads grouped in warps
  At most 32 warps
4 warp schedulers  4 warp instructions/cycle
  Need not belong to same block
  Picked from ready warps
Stalled warps: waiting for
  Memory
  Synchronization
  Long-latency instructions
Many threads/blocks  latency hiding

## Slide 25: Synchronization
Memory copy can be asynchronous
Kernel execution can be asynchronous
Synchronization levels
  Warp: implicit lockstep
  Block: explicit sync statement
  Cluster (H100+): cluster boundaries
  Grid: cooperative group kernel (all blocks must fit on GPU)
  GPU: kernel boundaries
Overlapping
Data transfers
Computations
 Explicit synchronization to avoid race conditions!!!

## Slide 26: Inquiry functions & configuration
Compute capability
Hardware limits
  Number of devices
  Maximum number of threads/block & dimension
  Memory/cache sizes
  

## Slide 27: Performance considerations
Avoid warp divergence (beware of branching)!
Ensure threads have enough work
Increase arithmetic intensity
Number of threads/block  registers/shared memory
  Ensure sufficient occupancy
Exploit data locality (shared memory/L2 cache)
Minimize host-device memory transfers and synchronization
Memory access matters  data access coalescing
  Accommodate 128-byte memory transactions
  Warp should access consecutive addresses  grid-trided loops to distribute work
  Data should be aligned
  Data layout  thread access pattern (e.g., SoA vs. AoS)
Note: opposite of CPU multithreading wisdom!

## Slide 28: Evolution

## Slide 29: Architecture & compute capability
Model | Architecture | Compute capability | NVLink version | PCIe version | Base frequency (GHz) | Boost frequency (GHz)
P100 | Pascal | 6.0 | 1.0 | 3.0 | 1.33 | 1.48
V100 | Volta | 7.0 | 2.0 | 3.0 | 1.20 | 1.53
A100 | Ampere | 8.0 | 3.0 | 4.0 | 0.77 | 1.41
H100 | Hopper | 9.0 | 4.0 | 5.0 | 1.67 | 1.83
B100 | Blackwell | 10.0 | 5.0 | 5.0+ | 1.80 | 2.00

## Slide 30: NVIDIA memory architecture
Level | P100 | V100 | A100 | H100 | B100
Registers | 64K  4b | 64K  4b | 256K  4b | 256K  4b | 256K  4b
Shared memory | 64Kb | 96Kb | 164Kb | 228Kb | 256Kb
L1 cache | 24Kb |  |  |  | 
L1 + shared | Separate | 128Kb | 192Kb | 256Kb | 256-288Kb
Const cache | 8Kb | 8Kb | 8Kb | 8Kb | 8Kb
L2 cache | 4Mb | 6Mb | 40Mb | 50Mb | 192Mb
Global | 16Gb | 32Gb | 80Gb | 80Gb | Up to 192Gb
Check cache size assumptions for kernels!

## Slide 31: NVIDIA SMs
Model | SMs | Cores per SM | Lanes (TF32/FP64/INT) | Tensor cores per SM | Tensor tile sizes
P100 | 56 | 64 | 64/32/64 | N/A | N/A
V100 | 80 | 64 | 64/32/64 | 8 (mixed FP16/FP32) | 4  4  4
A100 | 108 | 64 | 64/32/64 | 4 (FP16, BF16, TF32, FP64) | 16  8  8
H100 | 132 | 128 | 128/64/64 | 4 (FP8, FP16, BF16, TF32, FP64) | 64  64  16
B100 | 192 | 128 | 128/64/64 | 4 (FP4, FP8, FP16, BF16, TF32, FP64) | 64  64  32
E.g., for H100
FP32 peak  60 TFLOP/s
Fp8 tensor peak  2000 TFLOP/s
32 lanes  1 warp instruction/cycle
64 lanes  2 warp instructions/cycle
128 lanes  4 warp instructions/cycle

## Slide 32: NVLink & PCIe
Model | Links/GPU | GPU-GPU bandwidth (Gb/s) | PCIe bandwidth (Gb/s)
P100 | 4 | 40 to 80 (non-uniform) | 32
V100 | 6 | 50 (non-uniform) | 32
A100 | 12 | 200 | 64
H100 | 18 | 300 | 128
B100 | 18 | 600 | 128

## Slide 33: Impact on software
More memory  increase tile size
More L2 cache  ensure L2 locality
Tensor cores  exploit mixed precision
More instruction level parallelism  occupancy can decrease
Overlap memory transfer and computation
Profile!